1. ELCL documentation
   TODO
2. Car specification
   Cars are represented by an xml file and one or more png files.
  1. PNG files:
     Represents graphics, like wheels, car body, moving elements. Each png file should be mentioned in an xml file in order to be drawn.
  2. XML files:
     Car description file with the following nodes:
    1. <root>
       Every car must have such root node. Attributes:
Table 1: Car <root> attributes
Attribute	Values	Mandatory	Defaults to when not present	Notes
type	‘vehicle’ (string)	Yes	-	-

    1. <bodies>
       Contains a list of bodies that form a car. It is child of a <root> node. Usually at least main car body and wheels should be a separate bodies. It has no attributes.
    2. <body>
       Contains parameters of the car body. It is a child of the <bodies> node, and contains the following attributes:
Table 2: Car <body> attributes
Attribute	Values	Mandatory	Defaults to when not present	Notes
central	‘True’, ‘False’ (string)	Yes (for one body)	‘False’	One and only one body should have its ‘central’ attribute set to ‘True’. If true, this body will be treated as a central car body. Rotations will be applied to center of mass of this body, and other car bodies/shapes will be mirrored to this body when flipped.
rotational_force	‘20.0’ (float value)	No	20	How fast body will be rotated whel left/right rot keys are pressed. Only valid for ‘central’ body.
rotational_limit	‘2.0’ (float value)	No	2	Rotation limit. Only valid for ‘central’ body.
motor	‘True’, ‘False’ (string)	Yes (for at least one body)	‘False’	At least one body should have its ‘central’ attribute set to ‘True’. If ‘True’, this body will rotate when acceleration/deceleration key is pressed.
speed	‘20.0’ (float value)	Yes	-	How fast the body will rotate when acceleration/deceleration key is pressed (for deceleration half of the value is used). Only valid for ‘motor’ bodies.
acc	‘0.05’ (float value)	No	0.05	How fast body will gain rotational velocity. Only valid for ‘motor’ bodies.
differential_dest	‘id1 id2’ (space separated strings)	No	-	When differential mode is true, bodies mentioned in this attribute will receive the same rotational values as current body (this body acts as a driver to the destination bodies). Only valid for ‘motor’ bodies.
texture	‘tex.png’ (string)	Yes	-	Link to texture that will be drawn as this body.
type	‘DYNAMIC’, ‘STATIC’, / ‘KINEMATIC’ (string)	Yes	-	See pymunk documentation.
texture_flip_lr	‘True’ or ‘False’ (string)	No	‘True’	Set to ‘False’ if the car texture faces left.
texture_scale	‘2.0’ (float value)	No	1	Set if the texture should be draw scaled
position_x, / position_y	‘30.0’ (float value)	No	0	Initial body position. Important when setting constraints (bodies will be moved to their positions, and then constraints will be added).
position	‘20.0 30.0’ (two float values separated with a space)	No	0, 0	Initial body position (see above).
id	‘rightWheel’ (string)	Yes	-	Name of the body. Each such id should be unique in the file. It is used e.g. as differential destination, constraints also uses id to link bodies/shapes.
mass	‘20.0’ (float value)	No	Infinity	Mass of a body. It is set after shapes are added to body.
moment	‘20.0’ (float value)	No	Infinity	Moment of inertia of the body
start_angle	‘20.0’ (float value)	No	0	Sets starting angle of the body.

    2. <shape>
       Contains parameters of shapes that form a body. It is a child of the <body> node for which it will be added, and contains the following attributes:

Table 3: Car <shape> attributes
Attribute	Values	Mandatory	Defaults to when not present	Notes
id	‘wheelShape1’ (string)	Yes	-	Name of the shape. Each such id should be unique in the file. Constraints uses id to link bodies/shapes.
elasticity	‘1.0’ (float value)	No	0	How bouncy the shape is.
friction	‘0.9’ (float value)	Yes	0	Friction parameter.
density	‘123.0’ (float value)	No	0	If present and not zero, mass of the body will be updated by a volume and density of the shape
type	‘CIRCLE’, / ‘POLY’, / ‘SEGMENT’ (string)	Yes	-	What kind of body is it. See pymunk documentation and attribute description below.
a_x, a_y, b_x, b_y	‘1.0’ (float value)	Yes	-	X and Y coordinates of the segment. Only valid for the ‘SEGMENT’ shape.
offset_x, offset_y	‘2.0’ (float value)	Yes	-	X and Y coordinates of the circle. / Only valid for ‘CIRCLE’ shape.
radius	‘3.0’ (float value)	No	1	Radius of circle or thickness of segment. / Only valid for “CIRCLE’ and ‘SEGMENT’ shapes.
collision_type	‘1’ (32 bits or integer value)	No	-	When given, value of the collision type for this body can be used in a collision callback (pre/post/begin/end functions).
collision_group	‘0b110011’ (32 bits or integer value)	No	0	Shapes that have the same group do not generate collisions. Group with the value of 0 collides with everything (does not belong to any group).
collision_category	‘0b001100’ (32 bits or integer value)	No	0b11111111111111111111111111111111	Default, when not given, shapes belong to every category and collide with every category. When category is given, shape will collide with other shape, that has at least one bit in its mask that is in the current shape’s category.
collision_mask	‘0b0111000’ (32 bits or integer value	No	0b11111111111111111111111111111111

    1. ‘POLY’ <shape>
       This shape contains also text value in its node, which is a space separated set of float values (two values per vertex, x and y):
       val_x1 val_y1 val_x2 val_y2 … val_xn val_yn
       for example:
       <shape id="head" elasticity="0.9" friction="0.01" density="0.0" radius="1.0" type="POLY">0.0 0.0
       -90.0 10.0 0.0 40.0 90.0 20.0</shape>
       val_x and val_y are points that forms a vertex of the polygon. The polygon is closed, so it connects its last vertex with the first one.
    2. <constraints>
       Contains a list of body/shape constraints that links bodies/shapes together. It is child of a <root> node. Usually at least main car body and wheels should have a constraint, that will keep wheels bounded to the car frame.
    3. <constraint>
       Contains parameters of the individual constraint. It is a child of the <constraints> node, and contains the following attributes:

Table 4: Car <constraint> attributes
Attribute	Values	Mandatory	Defaults to when not present	Notes
id	‘constraint1’ (string)	Yes	-	Name of the constraint. Each such id should be unique in the file. Used internally.
a b	‘body_id’ (string)	Yes	-	Id of connected bodies.
type	One of: / ‘PinJoint’, ‘SlideJoint’, ‘PivotJoint’, ‘GrooveJoint’, ‘DampedSpring’, ‘DampedRotarySpring’, ‘RotaryLimitJoint’, ‘RatchetJoint’, ‘GearJoint’, ‘SimpleMotor’ (string)	Yes	-	See pymunk documentation for details.
anchor_a_x, anchor_a_y	‘4’ (float value)	Yes	-	Applicable to ‘PinJoint’, ‘SlideJoint’, ‘PivotJoint’, ‘DampedSpring’. See pymunk documentation for details.
anchor_b_x, anchor_b_y	‘4’ (float value)	Yes	-	Applicable to ‘PinJoint’, ‘SlideJoint’, ‘PivotJoint’, ‘GrooveJoint’, ‘DampedSpring’. See pymunk documentation for details.
groove_a_x, groove_a_y, / groove_b_x, groove_b_y	‘4’ (float value)	Yes	-	Applicable to ‘GrooveJoint’. See pymunk documentation for details.
distance	‘4’ (float value)	No	0	Applicable to ‘PinJoint’. See pymunk documentation for details.
min, max	‘2’ (float value)	Yes	-	Applicable to ‘SlideJoint’, ‘RotaryLimitJoint’. See pymunk documentation for details.
stiffness, damping	‘3’ (float value)	Yes	-	Applicable to ‘DampedSpring’, ‘DampedRotarySpring’. See pymunk documentation for details.
rest_length	‘6’ (float value)	Yes	-	Applicable to ‘DampedSpring’. See pymunk documentation for details.
rest_angle	‘0.12’ (float value)	Yes	-	Applicable to ‘DampedRotarySpring’. See pymunk documentation for details.
ratchet, angle	‘1’ (float value)	Yes	-	Applicable to ‘RatchetJoint’. See pymunk documentation.
phase	‘1’ (float value)	Yes	-	Applicable to ‘RatchetJoint’, ‘GearJoint’. See pymunk documentation for details.
ratio	‘1’ (float value)	Yes	-	Applicable to ‘GearJoint’. See pymunk documentation for details.
rate	‘2’ (float value)	Yes	-	Applicable to ‘SimpleMotor’. See pymunk documentation for details.
collide_bodies	‘0’ or ‘1’ (integer value)	No	0	If set to 1, bodies connected with this constraint can collide with each other.
max_bias, max_force	‘0.001’ or ‘inf’ (float value or string)	No	Default pymunk values	See pymunk documentation for details.
error_bias	‘0.001’ (float value)	No	Default pymunk values	See pymunk documentation for details.

Table 5: Car <constraint> examples
Constraint	Example
‘PinJoint’	<constraint id="lwDS" a="head" b="lw" type="PinJoint" anchor_a_x="-64.0" anchor_a_y="0.0" anchor_b_x="0.0" anchor_b_y="0.0" distance="0.0" />
‘SlideJoint’	<constraint id="lwDS" a="head" b="lw" type="SlideJoint" anchor_a_x="-64.0" anchor_a_y="0.0" anchor_b_x="0.0" anchor_b_y="0.0" min="0.0" max=”10.0” />
‘PivotJoint’	<constraint id="lwDS" a="head" b="lw" type="PinJoint" anchor_a_x="-64.0" anchor_a_y="0.0" anchor_b_x="0.0" anchor_b_y="0.0" />
‘GrooveJoint’	<constraint id="lwGJ" a="head" b="lw" type="GrooveJoint" groove_a_x="-64.0" groove_a_y="-30.0" groove_b_x="-64.0" groove_b_y="-60.0" anchor_b_x="0.0" anchor_b_y="0.0" />
‘DampedSpring’	<constraint id="lwDS" a="head" b="lw" type="DampedSpring" anchor_a_x="-64.0" anchor_a_y="0.0" anchor_b_x="0.0" anchor_b_y="0.0" rest_length="50.0" stiffness="20.0" damping="10.0" />
‘DampedRotarySpring’	<constraint id="lwDS" a="head" b="lw" type="DampedRotarySpring" rest_angle="0.1" stiffness="20.0" damping="10.0" />
‘RotaryLimitJoint’	<constraint id="lwDS" a="head" b="lw" type="RotaryLimitJoint" min="0.1" max="0.2" />
‘RatchetJoint’	<constraint id="lwDS" a="head" b="lw" type="RatchetJoint" phase="0.1" ratchet="20.0" angle="10.0" />
‘GearJoint’	<constraint id="lwDS" a="head" b="lw" type="GearJoint" phase="0.1" ratio="2.0" />
‘SimpleMotor’	<constraint id="lwDS" a="head" b="lw" type="SimpleMotor" rate="2.0" />

2. Level specification
  TODO
3. Enemy specification
  TODO